## Slide 1: Chapter 3 Sterilization & Disinfection
Sanitation
  Wash
Decontaminate
  Remove or destroys pathogens
Detergent
  soap
Disinfectant
  A chemical that removes pathogens
Spore
  A thick walled capsule around a germ
Sterilize
  Use a sterilizer or autoclave

## Slide 2: Hazardous Chemicals
MSDS sheets tell about hazardous chemicals. This one is about CIDEX
For example:
Cidex or Glutaraldehyde should be WASHED DOWN THE DRAIN
If it splashes in your eye you could FLUSH WITH WATER FOR 15 MINUTES

## Slide 3: STORING DISINFECTANTS
Shelf life
  EXPIRATION DATE
Use (& Reuse) life
  How long it is effective after being MIXED
    E.g. Cidex is good for 28 days after mixing
    Bleach good for ½ hour.

## Slide 4: Disinfectant levels
Level | Kills | Use | example
High | All microbes, virus & fungi except spores | Semi-critical items that go inside you e.g. a Flex sig | Glutaraldehyde (Cidex)
Intermediate | Most microbes, virus & fungi Except spores | Non – critical items that touch you e.g. stethoscope | alcohol
low | Most microbes but not TB or spores | Surfaces of tables etc. | Household bleach

## Slide 5: Types of Disinfectants
Glutaraldehyde
  E.g. Cidex
  Semi critical items that can’t be autoclaved
Alcohol
  70% solution is best
  Intermediate to low
  For Stethoscopes
Chlorine (bleach)
  10% solution is best
  Kills TB, HIV & hepatitis B &C
  Lasts for 10 minutes
  OSHA recommends it for blood spills
Phenolics
  For walls, furniture
  E.g. Lysol

## Slide 6: STERILIZATION
Fill out the log
  from page 111
Watch an autoclave demonstration
Care for the autoclave
Wipe inside and out with autoclave cleaner, rinse & dry
Clean and check the rubber gasket around the door
Only use distilled water

## Slide 7: Autoclave
On the wrap write:
  YOUR NAME,
  DATE
  WHAT’S INSIDE
Start timer when at right temperature
Muslin is best:
  lies flat
  can be reused.
Steam should get around the items & inside.
  1 to 4 inches apart
  Not touch the walls
  Jars on their side
  Lids removed

## Slide 8: Sterlization indicators
Autoclave tape
  On outside
  Changes color when exposed to steam
Sterilization strips
  Change color when exposed 250F for 15 minutes
  Should be placed in center of wrapped pack
Biologic indicators
  CDC says use once a week
  Live spores in small envelopes.
  Harmless to humans
  To see if it works, compare color of steamed ones with the control.

## Slide 9: Other sterilization methods
Dry heat oven
Used if steam would damage an item
320 for 1 or 2 hours
Cold sterilization
Only use chemicals rated “sterilants” by the EPA
Leave the instrument in it for 6 to 24 hours

## Slide 10: REVIEW
To Sterilize you :
  Use a sterilizer
To Disinfect you :
  Use chemicals
To Sanitize you:
  wash